## Slide 1: Electric Power Testing – Advanced Analysis
Get insights into your drive
Mitch Marks / Klaus Lang
Business Development Management – Electric Power Testing

## Slide 2: Examples
Vibration measurement
CAN bus correlation
dq0 & Space Vectors
Drive cycle power
Dynamic power
Dynamic torque
Torque ripple
In car drive cycle
Inverter Control Calibration

## Slide 3: Vibration Measurements in Electric Machines

## Slide 4: Correlate Vibration, Torque, and Electric Power
Voltage and current cause torque and vibration
Combined measurements help to correlate vibration, electrical, and rotational effects
In this example:
  Vibration increases with torque
  Vibration decreases with speed
Measurement of the electro- mechanical system
Vibration measured with voltage, current, torque, and speed. The machine is ramped in torque and speed to look at the vibration for each point.
– Acceleration – Current – Voltage
– Torque – Speed
HOME

## Slide 5: Synchronized CAN bus measurements

## Slide 6: CAN bus measurement – Comparison of control and reality
Acquisition and display of CAN control signals and their measured counterparts
Evaluate internal controller and sensors
Tune the system and make engineering decisions
Understand failures
Speed up development time and measure the whole system
CAN commands for torque and phase 1 current compared to their measured values. This test was performed on a malfunctioning machine
– Torque
– Torque CMD
– Speed
– Current
– Current CMD
HOME

## Slide 7: dq0 & Space Vector Transformations

## Slide 8: dq0 transformation in a live display
Real time dq0-transformation for a load step in an induction machine
Time domain display of d-,q-signals
Insight on what´s happening in the machine
Time synchronized to other signals
Load step in an induction machine. I_q and torque are directly related to one another
– I_d
– I_q
–Torque
HOME

## Slide 9: Drive Cycle Power Measurements

## Slide 10: User Driving Patterns Effect Efficiency
Increased losses in dynamic situations make drive cycle testing necessary
Testing the system the way a user will gives accurate range estimations
Cycle based power analyzer can accurately measure dynamic power
Dynamic power is needed to optimize the machine controller
Only possible with cycle based measurement
Dynamic signals from laps around a track on an electric scooter. Including: starts, stops, coasts, uphill and downhill
– Instantaneous Signals
– RMS Signals
HOME
– Power
– Reactive Power
– Apparent Power

## Slide 11: Dynamic Power Measurements

## Slide 12: Importance of Dynamic Power Measurement
At motor start, stop, or change of state there are losses associated with state change
Example of an inverter started induction machine
Large reactive power during the transient resulting in inefficiency
Dynamic power measurements needed to understand actual efficiency during use
Only possible with cycle detect
Current suddenly applied to an electric motor and associated power, reactive power, and apparent power for this dynamic load change
Reactive Power Spike
Current Inrush
– Power
– Reactive Power
– Apparent Power
– Current
– RMS Current
– Cycle detect

## Slide 13: Dynamic Power Starting
Inrush of current when vehicle starts
Voltage and current frequencies increase
Extra power and reactive power needed to start the vehicle
Overshoot of current, power, and reactive power at cursor
Scooter acceleration from 0 speed showing a ramp from 0 to full power.
Note back EMF and PWM operation.
Inrush Current
Power Overshoot
– Power
– Reactive Power
– Apparent Power
HOME
– Currents
– Cycle detect
– Voltages

## Slide 14: Dynamic Torque Measurement

## Slide 15: Properly Measuring Dynamic Torque
Torque from load steps has dynamic content
Torque responses often have overshoots and settling time
  Overshoots can harm the system
Filtered torque has phase delay and loses some amplitude info
Highly filtered torque has large phase delay and loses all amplitude and frequency info
Current –
Phase Delay
Load step for an electric machine and cyclical torque with different filter rates
– Currents
– Full Bandwidth Torque
– 100 Hz Filtered Torque
– 10 Hz Filtered Torque
HOME

## Slide 16: Torque Ripple

## Slide 17: Torque ripple  Dynamic torque in a steady state
Torque is not constant
  It always is a DC with an AC ripple
  Ripple has a cyclical nature
The ripple is a function of motor construction and excitation
  Slots
  Magnets
Ripple frequency is proportional to speed
Full measurement chain with understanding of all elements
Three phase motor excitation currents (red) and resultant torque ripple (blue)
36 ripples / electrical cycle
– Torque
– Currents

## Slide 18: Torque ripple  Effects of the Inverter
Control changes are a good opportunity to look at torque transients
Example: Control change from PWM to six step (smooth sine wave to jagged)
  Ripple frequency increases with control change
  Negative torque swings
Full measurement chain with understanding of all elements:
  Effect can be tied back to Vibration
Control change from PWM to 6 step
– Voltage
– Current
– Torque
HOME

## Slide 19: Voltage, Current, and Torque Frequency Content
Fundamental and rotational current and torque are similar
6 step current has significantly more current harmonic content in PWM
  5th , 7th, 11th, …
Torque has significantly more harmonic content during PWM
  4x, 5x, 8x, 10x, 12x rotational frequency
  Linked to current
Real time or post process FFT for system level understanding
Poles
5th electrical harmonic
Construction
Switching
PWM
6 step
PWM
6 step
Frequency spectrum comparing current and torque during PWM and 6 step operation

## Slide 20: In Vehicle Electric Power Measurement

## Slide 21: Real World Road Dynamics
Driving in different scenarios results in different current profiles
Power changing with environment or driver habits
Power fluctuations influence system efficiency
Understand control behavior to disturbances
Full Throttle
Coast
Downhill Acceleration
Scooter dynamics for full throttle, a coast, and downhill acceleration
– Current
– Voltage
– Power
– Reactive Power
– Apparent Power
HOME

## Slide 22: Inverter Control Calibration

## Slide 23: Space vectors to analyze control
The three currents i1, i2, i3 of a 3-phase system are represented with two linear independent vectors iα , iβ.
Doing so motor models are simplified
Control algorithms can be drafted more easily

## Slide 24: Space vector examples
HOME

## Slide 25: Mitch Marks / Klaus Lang Business Development Manager – Electric Power Testing mitchell.marks@hbkworld.com klaus.lang@hbkworld.com
File: HBM Electric Power Testing - Advanced analysis examples 2020 03